TA cloning using Pfu, Taq, and TOPO cloning kit

- Perform PCR reaction as normal using Pfu polymerase---if did PCR using Taq skip to step 4.

- Gel purify PCR fragment  (used Montage kit, but others probably will work fine)

- “Tail” the purified PCR fragment:  (adapted Promega pGEM cloning kit)

  - 1-7ul of PCR fragment (I usually use 5ul)

  - 1ul of Taq 10x Buffer with MgCl2

  - Add dATP to a final concentration of 0.2mM (create 2mM stock and add 1ul)

  - Add 5units (1ul) of Taq polymerase

  - Add water to final volume of 10ul

  - Incubate at 70-72C for 15-30min (easier in PCR machine vs heating block)

- Ligation---TOPO cloning kit is located in rm 319 on right-hand side freezer

  - 0.5-4.0ul of tailed PCR product (no need to purify again and I typically use 4ul)

  - 1ul of salt solution

  - 1ul of TOPO vector (tube contains vector and topoisomerase)

  - Add water to final volume of 6ul

  - Incubate at room temperature for at least 5min (longer doesn’t hurt)

  - OPTIONAL: adding 1ul of T4 DNA ligase increases yield but also the number of false positives

- Use 1-5ul of ligation for transformation